## Slide 1: 19CSE211-Computer Organization & Architecture

## Slide 2
Instruction Set Architecture
ISA-or simply architecture-is the abstract interface between the hardware and lowest level software that encompasses all the information necessary to write a machine level program including instructions, registers, memory accesses…
A very important abstraction
  advantage: enable implementations of varying cost and performance to run identical software
Common instruction set architectures:
  IA-64, IA-32, PowerPC, MIPS, SPARC, ARM, and others
  All are multi-sourced, with different implementations for the same ISA
Notes: 2

## Slide 3
Instruction Set Architecture (ISA)
The attributes of a computing system as seen by the programmer ,i.e conceptual structure and functional behaviour, as distinct from the organization of data flows and controls,the logic design and the physical implementation.[From Programmer’s point of view]
Computer Architecture(Programmer’s point of view)
ISA Includes
  Organization of storage
  Data types
  Encoding and representing instructions
  Instruction Set (i.e. opcodes)
  Modes of addressing data items/instructions
Notes: 3

## Slide 4
The Instruction Set: a Critical Interface
instruction set architecture
software
hardware
Notes: 4

## Slide 5
Computer Architecture- Block diagram
Computer
Architecture
I/O system
Instr. Set Proc.
Compiler
Operating
System
Application
Logic Design
Circuit Design
Instruction Set Architecture
Firmware
Implementation
Layout
Notes: 5

## Slide 6
MIPS-32 ISA
Instruction Categories
  Computational
  Load/Store
  Jump and Branch
  Floating Point
  Memory Management
  Special
R0 - R31
PC
HI
LO
Registers
op
op
op
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
Register format
Immediate format
Jump format
Opcode=6 bits, rs/rt/rd=5 bits each, immediate=16 bits and Jump address=26 bits, sa=5 bits and funct=6 bits